## Slide 1: Introduction to arduino

## Slide 2: Arduino
Arduino is the go-to gear for artists, hobbyists, students, and anyone with a gadgetry dream.
Arduino rose out of another formidable challenge: how to teach students to create electronics, fast.
With Arduino, you can control almost everything around you be it simple LED or giant Robots.

## Slide 3: Arduino
Basically Arduino is Microcontroller.
Microcontroller is microprocessor with memory, RAM and some other peripheral connected with it.
The Arduino Uno is a microcontroller board based on the ATmega328 . The ATmega328 has Flash memory of 32 KB (with 0.5 KB used for the bootloader). It also has 2 KB of SRAM and 1 KB of EEPROM
Notes: Flash- Where program is stored.
SRAM-Static Random Access Memory ( sketch creates and manipulates variables when it runs )
EEPROM- Electrically Erasable Programmable Read-Only Memory ( memory whose values are kept when the board is turned off )

## Slide 4: Different types of Arduino
Arduino Mega 2560
Arduino LilyPad
Arduino Uno
DIY Arduino
Boarduino Kit

## Slide 5: Arduino uno
What does it have?
  14 Digital In/Out pins (6 can be used as PWM)
  6 Analog Inputs
  A USB Connection
  A Power Jack
  Reset Button
  On-board LED
  SCL/SDA pins (Serial Clock/ Serial Data pins)
In short, it contains everything needed to support the microcontroller; simply connect it to a computer with a USB cable or power it with a AC-to-DC adapter or battery to get started.

## Slide 6
Digital I\O
PWM(3, 5, 6, 9, 10, 11)
SCL\SDA
(I2C Bus)
RESET
PWR IN
USB
(to Computer)
Analog INPUTS
POWER
5V / 3.3V / GND

## Slide 7: How to code in arduino
You need to download Arduino IDE (Integrated Development Environment).
Arduino IDE is available for all Mac, Windows.and Linux.

## Slide 8: How to code in arduino
Once you have downloaded and installed/extracted the folder, you can directly run Arduino.exe, which will take you to its IDE.
The IDE will look like the shown screenshot.
error & status messages

## Slide 9: Program your arduino
Before you start programming, double check that correct board is selected under Tools  Board.
Now, you can start playing with Arduino.

## Slide 10: Program your arduino
The Arduino Uno can be programmed with the Arduino software. Select "Arduino Uno from the Tools > Board menu (according to the microcontroller on your board).
All the peripheral connected with Computers are using Serial Port.
You can check port for Arduino Uno in Device Manger.

## Slide 11: Input vs output
Image from Theory and Practice of Tangible User Interfaces at UC Berkley

## Slide 12: 6 Major concepts
digitalWrite()
analogWrite()
digitalRead()
If (statements) / Boolean
analogRead
Serial Communication

## Slide 13: Analog vs digital
Microcontrollers are digital devices – ON or OFF. Also called – discrete.
Analog signals are anything that can be a full range of values.
5 V
0 V
5 V
0 V

## Slide 14: Analog vs digital
Analog Sensors
Sensors | Variables
Mic | soundVolume
Photoresistor | lightLevel
Potentiometer | dialPosition
Temp Sensor | temperature
Flex Sensor | bend
Accelerometer | tilt/acceleration
Digital Sensors
  Digital sensors are more straight forward than Analog.
  No matter what the sensor there are only two settings: On and Off
Example, Push button, Switch

## Slide 15: Serial communication
“Serial” because data is broken into bits, each sent one after another in a single wire.
Compiling turns your program into binary data (ones and zeros)
Uploading sends the bits through USB cable to the Arduino
The two LEDs near the USB connector blink when data is transmitted.
  RX blinks when the Arduino is receiving data.
  TX blinks when the Arduino is transmitting data

## Slide 16: Let’s start coding

## Slide 17: Project #1 led blink
digitalWrite()

## Slide 18
Compile
Upload
Status Message

## Slide 19: Thank you
Pune Makers
16th May 2015